Tate Access Floors, Inc.

Autocloser

SECTION 09 69 00

Access Flooring Accessories

2.4	Accessories

Autocloser:

Aisle containment Autocloser shall be factory provided with the following specifications:

  - Finish: Frame brackets shall be constructed of [clear anodize aluminum] [black anodize aluminum]. Autocloser body shall constructed of clear anodize aluminum.

  - Dimensions: Autocloser shall have a body size diameter of no more than 1.75”. Body shall be able extend from 21.25” to 51.5” allowing for compatibility with a wide range of door sizes.

  - Design Features: Autocloser shall not require any permanent modifictions to either sliding door or door frame. Autocloser shall not be visible when door is closed position. Autocloser shall be available for use with both single and double door systems. Autocloser shall have an adjustable return rate to allow for smooth door operation. A hold open option shall be available.