Tate Access Floors, Inc.

Containment Dual Hinged Door

SECTION 09 69 00

Access Flooring Accessories

2.4	Accessories

Solid Doors:

Dual Hinged Door:

Aisle containment Dual Sliding Door shall be factory provided with the following specifications:

  - Finish: Frame shall be constructed of [white aluminum] [black aluminum][grey aluminum].

  - Dimensions: Dual Hinged Door frame shall have a max height of 96” max width of 72” and a depth of 4.55”

  - Design Features:

    - Dual Hinged door to be [right hinged][left hinged]

    - Viewing Panels shall be [6mm thick clear polycarbonate with edge sealing gaskets and meeting ASTM D-635 Listed] [6mm thick semi-transparent multiwall polycarbonate with edge sealing gaskets and meeting ASTM E-84 Listed and UL 94 Listed].

    - Aluminum frame shall be constructed from 6063-T6 alloy. Frame to be of no threshold design to minimize trip hazard

    - Dual door system shall come packaged in pre-assembled sections with factory installed perimeter compression gasket system to efficiently seal and minimize air leakage

    - Shall have ergonomic handles that reduce pinch points

    - Aisle containment doors shall be fully supported at the base of the frame and have the ability to attach to the equipment racks or other aisle containment components for lateral securement

    - [ Dual hinged doors with multiwall polycarbonate are listed in UL file SA44425]