SECTION 09 69 00

ACCESS FLOORING ACCESSORIES

2.4	ACCESSORIES

AUTOCLOSER:

Aisle containment Autocloser shall be factory provided with the following specifications:

  - Finish: Frame brackets shall be constructed of [clear anodise aluminum] [black 
anodise aluminum]. Autocloser body shall constructed of clear anodise aluminum.

  - Dimensions: Autocloser shall have a body size diameter of no more than 4cm. Body shall be able extend from 53cm to 130cm allowing for compatibility with a wide range of door sizes.

  - Design Features: Autocloser shall not require any permanent modifications to either 
sliding door or door frame. Autocloser shall not be visible when door is closed position. Autocloser shall be available for use with both single and double door systems. 
Autocloser shall have an adjustable return rate to allow for smooth door operation. 
A hold open option shall be available.