SECTION 09 69 00

ACCESS FLOORING ACCESSORIES

2.4	ACCESSORIES

Autocloser:

Aisle containment Autocloser shall be factory provided with the following specifications:

  - Finish: Frame brackets shall be constructed of [clear aluminum] [black painted aluminum]. Autocloser body shall constructed of [clear anodised aluminum] [black anodised aluminum]

  - Dimensions: Autocloser assembly shall have a footprint size of no more than 1.75” x 12.75” (4.45cm x 32.38cm).

  - Design Features: Autocloser shall not require any permanent modifictions to either hinged door or door frame. Autocloser shall not be visible when door is closed position. Autocloser shall be available for use with both single and double door systems. Autocloser shall have an adjustable return rate to allow for smooth door operation. A hold open option shall be available.