SECTION 09 69 00

ACCESS FLOORING ACCESSORIES

2.4	ACCESSORIES

SOLID DOORS:

Single Hinged Door:

Aisle containment Single Sliding Door shall be factory provided with the following specifications:

  - Finish: Frame shall be constructed of [clear anodise aluminum] [black anodise aluminum].

  - Dimensions: Single Hinged Door frame shall have a height of 86” (218cm) a width of 66.5” (167cm) and a depth no greater than 3.15” (8cm).

  - Design Features:

    - Single Hinged door to be [right hinged][left hinged].

    - Viewing Panels shall be [6mm thick clear polycarbonate with edge sealing gaskets and meeting ASTM D-635 Listed] [6mm thick semi-transparent multiwall polycarbonate with edge sealing gaskets and meeting ASTM E-84 Listed and UL 94 Listed].

    - Aluminum frame shall be constructed from 6063-T6 alloy. Frame to be of no threshold design to minimise trip hazard.

    - Single door system shall come packaged in pre-assembled sections with factory installed perimeter compression gasket system to efficiently seal and minimize air leakage.

    - Shall have ergonomic handles that reduce pinch points.

    - Aisle containment doors shall be fully supported at the base of the frame and have the ability to attach to the equipment racks or other aisle containment components for lateral securement.

    - [ Single hinged doors with multiwall polycarbonate are listed in UL file SA44425].